##### Interfaces Specification

A) 	General Information:

- Service provided on the highly reliable SDH/WDM infrastructure in the Central and Eastern Europe (CEE) region.

- Transmission and service quality is guaranteed as per international ITU-T standards.

- Services are provided in speeds 64 kbps - 2,5 Gbps based on customer requirements.

B)	Supported Speeds, Interfaces and Specifications

| Interface | Speed | Description | Connector |
| --- | --- | --- | --- |
| X.21 | 64 kbps n ( 64 kbps 1 984 kbps 2 048 kbps | Interface between data terminal equipment and data circuit-terminating equipment for synchronous operation on public data networks | DB-15F |
| V.24 | 64 kbps | List of definitions for interchange circuits between data terminal equipment (DTE) and data circuit - terminating equipment (DCE) | DB-25F |
| V.35 | 64 kbps n ( 64 kbps 1 984 kbps 2 048 kbps | Data transmission at 48 kilobits per second using 60-108 kHz group band circuits | AMP-34F |
| G.703 | 64 kbps 2 048 kbps 34 Mbps 155 Mbps | Physical / electrical characteristics of hierarchical digital interfaces | RJ45, BNC |
| G.703/G.704 | 64 kbps n ( 64 kbps 1 984 kbps | Synchronous frame structures used at 1544, 6312, 2048, 8488 and 44736 kbit/s hierarchical levels | RJ45, BNC |
| G.957 | 155 Mbps 622 Mbps 2,5 Gbps | Optical interfaces for equipment and systems relating to the synchronous digital hierarchy | E2000 |

C)         Other Supported Specifications

| Standard Organization | Standard Number | Characteristic |
| --- | --- | --- |
| ITU-T | M.1040 | Characteristics of ordinary quality international leased circuits |
|  | M.1025 | Characteristics of special quality international leased circuits with basic bandwidth conditioning |
|  | M.1020 | Characteristics of special quality international leased circuits with special bandwidth conditioning |
|  | J.21 | Performance characteristics of 15 kHz-type sound-programme - Circuits for high quality monophonic and stereophonic transmission |
|  | J.23 | Performance characteristics of 7 kHz type (narrow-bandwidth) sound-programme circuits |
|  | M.1370 | Bringing-into-service of international data transmission systems |
|  | M.1340 | Performance allocations and limits for international data transmission links and systems |
|  | G.826 | Error performance parameters and objectives for international, constant bit rate digital paths at or above the primary rate |
|  | G.827 | Avaibility parameters and objectives for path elements of international constant bit rate digital paths at or above the primary rate. |
|  | G.821 | Error performance of an international digital connection operating at a bit rate below the primary rate and forming part of an integrated services digital network |